GW2 Archive Format

The GW2.dat file is an archive of all resources that the GW2 client uses. It contains everything from the text used in-game, to models and shaders. In this document I will discuss the format of this file and how you can read and extract its contents. The order in which I discuss things may not be the order in which they appear in the archive, but rather in the suggested order you process them.

Notes:
- From this point forward, the GW2.dat file will be referred to as the archive to prevent confusion with the files that it contains.
- Github user Ahom has created a C++ library to which interfaces with the archive, and you can find it here. For help using this library, see the “How to Use the GW2.dat Tools Library” document.
- All numbers in the archive are arranged in little-endian fashion. This means that the memory block [50x, 45x] actually represents the number 4550x.
- When I list values by Byte #, 0 is the first byte that appears when reading the file. When I list values by Bit #, 0 is the highest value bit within the construct after it is read.
- All numbers in this document are in decimal, unless otherwise specified. Hexadecimal numbers will be followed by a subscript x (1Ax), octal numbers by a subscript o (32o), and binary by a subscript b (11010b). Sometimes a hexadecimal number will instead be represented as a character (i.e. 'A'). The value of this character is its ASCII code.
- I do not condone use of this document to modify the archive for any reason. Modifying the archive is a direct violation of the Terms of Service you agreed to follow when you bought the game.

# Archive Header
The archive begins with a 40-byte-long header with the following format:

Byte #	Size	Value	Description
0	1	Version	Version of the archive.
1	3	Identifier	Identifies the file as a GW2 data file. Always [41x, 4Ex, 1Ax].
4	4	Header Size	Size of this header. Always 40.
8	4	(unknown)
12	4	Chunk Size	Size of each chunk in the file. Always 512.
16	4	CRC	Was the CRC of the first 16 bytes of this header. Its current function is unknown.
20	4	(unknown)
24	8	MFT Offset	Offset of the Main File Table from the start of the file.
32	4	MFT Size	Size of the Main File Table in bytes.
36	4	Flags

# Main File Table (MFT)
The archive header is followed by the Main File Table (MFT). It's important to note that this does not necessarily directly follow the Archive Header. For example, the MFT in the version I'm using is 2886009856 Bytes (2.68GB) from the start of the file, which is a significant leap from the end of the Archive Header. The MFT contains information on and pointers to every file and table in the database.

The MFT is started with a 24-byte-long header with the following format:

Byte #	Size	Value	Description
0	4	Identifier	Identifies the start of the MFT header. Always ['M','f','t',1Ax].
4	8	(unknown)
12	4	Num. Entries	Number of entries in the table plus 1.
16	8	(unknown)

Directly following this are all of the entries in the MFT. Each entry is also 24 bytes long, and has the following format:

Byte #	Size	Value	Description
0	8	File Offset	Offset of the file represented by this entry from the beginning of the file.
8	4	In-Archive Size	Size of the file represented by this entry as it appears in the archive. If the file is compressed, this is the compressed size.
12	2	Compression	The type of compression this file is under. See below for values.
14	2	Flags	Various flags that further describe the file or this entry. See below for a list of valid flags.
16	4	(unused)	In GW1's archive file, this was a counter. Now, it is always 0.
20	4	(unknown)	In GW1's archive file, this was the CRC of the entry. Now its function is unknown. For all non-reserved entries, the value is 1214729159.

Valid values for the Compression item of the MFT entries include the following:
0x	Uncompressed
8x	Compressed

Valid flags that can be used in the Flags item of the MFT entries include the following:
1x	In Use
2x	???

The first 15 entries of the MFT are reserved, and include some special entries that point to other portions of the archive which further describe the files contained. These always appear in the same order in the MFT, and I'll describe them here. They are 1-indexed.
1	Archive Header
2	File ID Table
3	MFT Table (self reference)
4-15	Blank entries.

The File Offset value does not have any relation to the entry's MFT index.

# File ID Table
The File ID Table connects MFT Entries with their file's ID. Every entry in the File ID Table represents a single file. A File ID Table entry is 8 bytes long and is formatted as follows:

Byte #	Size	Value	Description
0	4	File ID	The File ID of this file.
4	4	MFT Entry Index	The index of the entry in the MFT that represents this file. Indices start at 1.

It is possible for either value to be zero, in which case the entry should be ignored. None of the entries have any relation between their indices in the File ID Table, their indices in the MFT, nor their File IDs. No two entries share the same File ID, but MFT Indices may be shared between at most two entries. Note that these two entries need not and often are not sequential, and the higher of the two IDs may appear after the lower. More research must be done into how pairs of files are represented by a single MFT Entry.

Some files will refer to other files via their File ID, but the only way to access a file is through its pointer in its entry in the MFT. Therefore, it is advisable to set up a mapping between File ID and MFT Index and vice versa in order to save a search through the File ID Table for either.

# File Headers and Formats
Each file begins with a header. This header begins at the file's offset, is 8 bytes long, and has the following format:

Byte #	Size	Value	Description
0	4	File Type	Defines the type of file. See below.
4	4	Uncomp. Size	The uncompressed size of this file.

Valid values for File Type are as follows:

Type FourCC	Type Value	Type Name
['P', 'F', ~~x, ~~x]	~~~~4650x	Pack File (The last two bytes may be anything)
['D', 'D', 'S', 20x]	20534444x	DirectDraw Surface Texture (DDS)
['A', 'T', 'E', 'P']	50455441x	ATEP (Map Texture)
['A', 'T', 'E', 'U']	55455441x	ATEU (UI Texture)
['A', 'T', 'E', 'X']	58455441x	ATEX (Generic Use Texture)
['<', 'S', 't', 'a']	6174533Cx	(unknown)
['a', 's', 'n', 'd']	646E7361x	Sound File (un-packed)
['<', '?', 'x', 'm']	6D783F3Cx	(unknown)
['s', 't', 'r', 's']	73727473x	Strings File
['M', 'Z', ~~x, ~~x]	~~~~5A4Dx	Binary File (The last two bytes may be anything)

There are also many unidentified file types that are used only a few times within the archive. File compression is done using Huffman codes with predefined frequencies. Ahom's library provides a decompression function for archive files.

In the next sections, I will describe the formats of the individual file types. The formats are described beginning after the general file header.

## Strings File Format
Strings files are stored as an array of string entries. The size of the array is not stated, a string entry does not have a standard size, and there is nothing indicating the end of the array, so you must parse all of the entries in order to determine the number of entries. The file has the following format:

Byte #	Size	Value	Description
0	4	File Type	Identifies the type of string file. This is identical to the File Type value in the general file header.
4	6+	String Entry	A string entry, which must be at least 6 bytes long.
(...)	(...)	More String Entries	The rest of the array of string entries.
Size-2	1	Language	The language the strings are written in. Valid values are listed below.
Size-1	1	Unknown	???

Valid values for Language include the following:
0	English
1	Korean
2	French
3	German
4	Spanish

String entries have the following format:

Byte #	Size	Value	Description
0	2	Size	The length in bytes of the entry, including these two bytes.
2	2	Decryption Offset	The function of this value is unknown, but if its value is not zero, the string is encrypted.
4	2	Bits Per Symbol	The number of bits per character. If its value is not 16, the string is encrypted.
6	Size-6	String	The UTF-16 encoded string value of this entry.

Entries where the Decryption Offset is not zero or the number of Bits Per Symbol is not 16 are encrypted. It is unknown how to decrypt such entries.

## ATEP (Map), ATEU (UI), ATEX (Generic Use) Texture File Formats
All textures are stored as arrays of compressed mipmaps. They begin with a 12-byte header defining their type, format, height, and width.

Byte #	Size	Value	Description
0	4	File Type	Identifies the type of texture file. This is identical to the File Type value in the general file header.
4	4	Format	The format of the texture file. Valid values are listed below.
8	2	Width	Width of the main texture.
10	2	Height	Height of the main texture.

Valid values for Format include the following:
31545844x	'DXT1'
32545844x	'DXT2'
33545844x	'DXT3'
34545844x	'DXT4'
35545844x	'DXT5'
41545844x	'DXTA'
4C545844x	'DXTL'
4E545844x	'DXTN'
58434433x	'3DCX'

This header is followed by an array of mipmaps, beginning with the full size texture. Each successive image is half the width and half the height of its predecessor. The number of mipmaps in the file is determined by the file's size. The images have the following format:

Byte #	Size	Value	Description
0	4	Size	Size of the following pixel array.
4	4	Compression Flags	Flags indicating what has been compressed. See below for valid values.
8	Size	Pixel Data	A block of pixel data. The format is determined by the Format value of the Texture Header.

Valid compression flags include the following:
1x	White Color
2x	4-bit Alpha (mutually exclusive with 8-bit Alpha)
4x	8-bit Alpha (mutually exclusive with 4-bit Alpha)
8x	Plain Color

The pixel data is compressed using Huffman codes. Ahom's library provides a function for decompressing mipmaps.

The size of the uncompressed pixel data depends on the width, height, and format of the file. It can be determined by the following formula:

Uncompressed Size = ⌈width / 4⌉ * ⌈height / 4⌉ * pixel block size

where ⌈x⌉ is the smallest integer greater than or equal to x (also known as the ceiling function/rounding up). The pixel block size is determined by the format. For formats DXT1 and DXTA, there are 8 bytes per pixel. For all other formats, there are 16 bytes per pixel block.

The uncompressed pixel data is not simply an array of pixel values. Instead, the image is broken into 4x4 pixel blocks, which fill the image from left to right, then top to bottom. The length of a pixel block is as defined above. The format of the pixel blocks and how they are processed is more varied than the size, however. I'll cover each one in turn here.

### Common Formatting
There are certain formatting properties that multiple formats share. I will describe them here rather than repeat the data in every formatting section.

First, pixels in the pixel block are always listed from right-to-left, then bottom-to-top. So you have pixels <3,3>, <2,3>, <1,3>, <0,3>, <3,2>, … <0,0>. Each pixel is described with an array of colors and alphas, only colors, or only alphas. The way pixels are assigned values varies, with some formats providing unique values for every pixel, and others generating a smaller set of values that pixels will share.

RGB values are represented in the pixel block by 2 bytes, and have the following format:

Bit #	Size	Value
0	5	Red
5	6	Green
11	5	Blue

Generally, there are 4 RGB values available to each block, and they are described using two RGB values stored in the block. In the generation of RGB values, alpha values are also generated. These are discarded unless the format uses deduced alpha values. Most formats discard these values, as they use explicit alpha values.

If the format is not DXT1, the Color Value List is written as follows:
0	Color1 * <255/31, 255/63, 255/31>, deduced alpha 255
1	Color2 * <255/31, 255/63, 255/31>, deduced alpha 255
2	linear interp( Color1, Color2, 1/3 ) * <255/31, 255/63, 255/31>, deduced alpha 255
3	linear interp( Color1, Color2, 2/3 ) * <255/31, 255/63, 255/31>, deduced alpha 255
Otherwise, the Color Value List is written as follows:
0	Color1 * <255/31, 255/63, 255/31>, deduced alpha 255
1	Color2 * <255/31, 255/63, 255/31>, deduced alpha 255
2	linear interp( Color1, Color2, 1/2 ) * <255/31, 255/63, 255/31>, deduced alpha 255
3	<0,0,0>, deduced alpha 0

Note that the scale attached to the end of each value simply translates a 5-bit or 6-bit color channel to an 8-bit channel.

Explicit alpha values are either 4-bit or 8-bit. 4-bit Alpha Values are described as an array of 16 values, taking up a total of 8 bytes. There is one value for each pixel. The value used by the pixel is actually the 4-bit value repeated twice to make an 8-bit value. In other words, if the 4-bit value is Ax, the used value is Aax. 4-bit value 5x translates to 55x, etc.

8-bit Alpha Values are described using two 8-bit base values. This allows up to 8 different alpha values, and is accompanied by a 6-byte array of 3-bit indices into this list of alpha values – one for each pixel.

If Alpha1 > Alpha 2, the Alpha Value List is written as follows:
0	Alpha1
1	Alpha2
2-7	linear interp( Alpha1, Alpha2, (i-1)/7 )
Otherwise, the list is written as follows:
0	Alpha1
1	Alpha2
2-5	linear interp( Alpha1, Alpha2, (i-1)/5 )
6	0x
7	FFx

### DXT1 Format
Each block in a DXT1 formatted texture file uses deduced alpha values, and has the following format:

Byte #	Size	Value	Description
0	2	Color1	One cap of a linear interpolation of color values.
2	2	Color2	The cap of a linear interpolation of color values.
4	4	Color Indices	An array of 2-bit indices into the list of available color values. There is one index for every pixel in the block.

### DXT2, DXT3, DXTN Format
Each block in a DXT2, DXT3, or DXTN formatted texture file uses explicit 4-bit alpha values, and has the following format:

Byte #	Size	Value	Description
0	8	Alpha Values	An array of 4-bit alpha values. There is one value for every pixel in the block.
8	2	Color1	One cap of a linear interpolation of color values.
10	2	Color2	The other cap of a linear interpolation of color values.
12	4	Color Indices	An array of 2-bit indices into the list of available color value. There is one index for every pixel in the block.

### DXT4, DXT5 Format
Each block in a DXT4 or DXT5 formatted texture file uses explicit 8-bit alpha values, and has the following format:

Byte #	Size	Value	Description
0	1	Alpha1	One cap of a linear interpolation of alpha values.
1	1	Alpha2	The other cap of the linear interpolation of alpha values.
2	6	Alpha Indices	An array of 3-bit indices into the list of available alpha values. There is one index for every pixel in the block.
8	2	Color1	One cap of a linear interpolation of color values.
10	2	Color2	The other cap of the linear interpolation of color values.
12	4	Color Indices	An array of 2-bit indices into the list of available color values. There is one index for every pixel in the block.

### DXTA Format
Each block in a DXTA formatted texture file allows 8 different RGB values that the pixels it represents may use. Strangely enough, this format only represents one color channel. The values available are generated in the same way as explicit 8-bit alpha values. It has the following format:

Byte #	Size	Value	Description
0	1	Value1	One cap of a linear interpolation of channel values.
1	1	Value2	The other cap of the linear interpolation of channel values.
2	6	Value Indices	An array of 3-bit indices into the list of available channel values. There is one index for every pixel in the block.

### DXTL Format
Each block in a DXTL formatted texture file uses explicit 8-bit alpha values, and has the following format:

Byte #	Size	Value	Description
0	1	Alpha1	One cap of a linear interpolation of alpha values.
1	1	Alpha2	The other cap of the linear interpolation of alpha values.
2	6	Alpha Indices	An array of 3-bit indices into the list of available alpha values. There is one index for every pixel in the block.
8	2	Color1	One cap of a linear interpolation of color values.
10	2	Color2	The other cap of the linear interpolation of color values.
12	4	Color Indices	An array of 2-bit indices into the list of available color values. There is one index for every pixel in the block.

### 3DCX Format
3DCX formatted texture files only specify red and green channel values. The red and green values available are generated in the same way as explicit 8-bit alpha values. A blue value is calculated for each pixel based on its red and green values and has the following format:

Byte #	Size	Value	Description
0	1	Green1	One cap of a linear interpolation of green values.
1	1	Green2	The other cap of the linear interpolation of green values.
2	6	Green Indices	An array of 3-bit indices into the list of available green values. There is one index for every pixel in the block.
8	1	Red1	One cap of a linear interpolation of red values.
9	1	Red2	The other cap of the linear interpolation of red values.
10	6	Red Indices	An array of 2-bit indices into the list of available red values. There is one index for every pixel in the block.

The following formula is used to calculate the blue value for a pair of red and green values:

blue = (FF/2) + √ (FF/2)2 – (red – FF/2)2 – (green – FF/2)2

If the value inside the square root is less than zero, the blue value is 0. The set of colors available for representation in the format is illustrated to the right:

## DDS Texture File Format
The DDS texture file format...

## Unpacked Sound File Format
The unpacked sound file format...

## Pack File Format
Pack files are stored as a list of chunks, with each chunk storing different information. There are different types of Pack Files – some store maps, some store sound, others store models. The content type is defined in the header, and each type of content has a different set of chunks that come with it. Each chunk has a unique identifier that defines the data it holds. Only one chunk of any particular ID is allowed in a Pack File at a time.

All Pack Files begin with a 12 byte long header:

Byte #	Size	Value	Description
0	2	Magic	Always 'PF'
2	2	Descriptor Type	?
4	2	Zero	Always 0
6	2	Header Size	Always 12
8	4	Type	Type of content in the Pack File. Valid values are listed below.

The Pack File's chunks follow this. Chunks do not have a set size to them. Instead, each chunk has a reference to the next chunk. They begin with a 16 byte long header as described below. The data that follows is dependent on the chunk's type.

Byte #	Size	Value	Description
0	4	Content Type	Type of chunk
4	4	Next Chunk Offset	Number of bytes after the end of this value the next chunk appears.
8	2	Version	???
10	2	Header Size	Always 16
12	4	Descriptor Offset	???

There are many different kinds of Pack Files. I'll list their Types here, then discuss each one and its set of chunks in turn.

Type FourCC	Type Value	Type Name
['a', 'n', 'i, 'c']	63696E61x	Animation Sequence
['A', 'S', 'N', 'D']	444e5341x	Audio
['A', 'B', 'I', 'X']	58494241x	Bank Index
['A', 'B', 'N', 'K']	4b4e4241x	Bank
['c', 'm', 'a', 'C']	43616d63x	Collide Model Manifest
['c', 'm', 'p', 'c']	63706d63x	Composite
['c', 'n', 't', 'c']	63746e63x	Content Manifest
['e', 'm', 'o', 'c']	636f6d65x	Emote Animation
['e', 'u', 'l', 'a']	616c7565x	EULA
['h', 'v', 'k', 'C']	436b7668x	Havok
['m', 'M', 'e', 't']	74654d6dx	Map Metadata
['m', 'a', 'p', 'c']	6370616dx	Map
['m', 'p', 's', 'd']	6473706dx	Map Shadow
['A', 'M', 'A', 'T']	54414d41x	Material
['M', 'O', 'D', 'L']	4c444f4dx	Model
['P', 'I', 'M', 'G']	474d4950x	Paged Image
['p', 'r', 'l', 't']	746c7270x	Portal Manifest
['C', 'I', 'N', 'P']	504e4943x	Scene
['A', 'M', 'S', 'P']	50534d41x	Script
['t', 'x', 't', 'm']	6d747874x	Text Manifest
['t', 'x', 't', 'V']	56747874x	Text Variant
['t', 'x', 't', 'v']	76747874x	Text Voice

Any Pack File Type not listed here is either invalid or unknown.

### Animation Sequence File Format
blah

### Audio File Format
blah

### Bank Index File Format
blah

### Bank File Format
blah

### Collide Model Manifest File Format
blah

### Composite File Format
blah

### Content Manifest File Format
blah

### Emote Animation File Format
blah

### EULA File Format
The EULA Pack File has only one chunk, whose type FourCC is 'eula' (616c7565x), appropriately. The chunk is an array of multiple versions of the EULA in different languages. It is begun by a header defining how many translations exist, and where in the chunk each one is. The header has the following format:

Byte #	Size	Value	Description
0	4	Count	Number of translations in this chunk.
4	4	Offset	How far the beginning of the translation array is from the beginning of this value. Always 8.
8	4	Version	Version of the EULA.
12	1	Translation 1 Language	The language that Translation 1 is written in.
13	4	Translation 1 Offset	How far the beginning of Translation 1 is from the beginning of this value.
17	5...	More Translations	The rest of the Translation languages and offsets. There are a total of (Count) language + offset pairs.

You can calculate the size of the header in bytes with the following formula:

Header Size = 12 + 5*Count
Each translation offset points to a UTF16 formatted C String – that is to say, it is ended by a null character and has no other indication of its size.
### Havok File Format
blah

### Map Metadata File Format
blah

### Map File Format
blah

### Map Shadow File Format
blah

### Material File Format
blah

### Model File Format
Model Pack Files contain 6 different chunks, which are identified as follows:

Type FourCC	Type Value	Type Name
['A', 'N', 'I', 'M']	1x	Animation
['M', 'O', 'D', 'L']	1x	Data (?)
['G', 'E', 'O', 'M']	1x	Geometry
['P', 'R', 'P', 'S']	1x	Properties
['R', 'O', 'O', 'T']	3x	Root Motion
['S', 'K', 'E', 'L']	3x	Skeleton

These chunks may be listed in any order. I'll go through each one here and describe it in detail.

Animation Chunk
blah

Model Data
blah

Geometry Data
The geometry chunk

Properties Data
blah

Root Motion Data
blah

Skeleton Data
blah
### Paged Image File Format
blah

### Portal Manifest File Format
blah

### Scene File Format
blah

### Script File Format
blah

### Text Manifest File Format
blah

### Text Variant File Format
blah

### Text Voice File Format
blah

# Special Thanks
I'd like to thank Github users Ahom and Rhoot for their efforts in reverse-engineering the archive and internal file formats. While they did not actively participate in the making of this documentation, their code provided the best insights I've had into the archive. Ahom provided the decompression functions that I could have never made myself, and they allowed me to further my research and documentation despite not having the technical expertise to write a decompression algorithm nor document it fully. Rhoot has reverse-engineered almost every relevant internal file format known to date. All of the documentation I have written is based off of his code in both his GW2Browser program and his gw2formats library.